1963 Studebaker Avanti

Model type

R-1

Serial No

63R1229 ( The 229th Avanti ever built)

Built by

Studebker motor Company

Build Date

September 1962

Plant Location

South bend, IN

Dealer/Delivery date

McVey Motors, Bethesda, MD, Oct 12, 1962

Original Owner

Dr. harry Fletcher MD, Silver Spring, MD

Second and cxurrent Owner ( Last 30 years)

Jim and Susie Pearce, lakel;and, FL

Purchase by Jim Pearce

April 1969

Original Engine

289cid, 240 HP Studebaker R-1, four barrel V8 (Not to be confused with the ford 289)

Delivered price

$5385.82  (Oct 1962)

Standard Equipment

- Fibreglass Body

- Power Front Disc Brakes

- Safety padded dash

- 289 cid V8, 4 barrel carb

- Two Speed Windshield Wipers

- Front Seat belts

Optional Equipment

- Air Conditioning

- Power Steering (16:1 ratio)

- Power Windows

- Windshield Washers

- Rear Seat belts

- Twin Traction

- Tinted Glass

- Rear Speaker

- AM Push Button Radio

Exterior Color

- Original Color: Avanti White

- Present Color: 1986 Corvette :Artic White” ( Painted by Jim Pearce using two stage Sikens paint)

Interior Color

- Fawn and Elk (Original and present)

Front Suspension

- Delrin Control Arm bushings with zerk fittings

- Gabriel Gas Shocks

- One Inch Sway bar

- Quick Steering Arms

- Rebuilt King Pins ( New bushings/bearings)

- Rebuilt Bell-Crank assembly

- New Power Steering Control Valve assembly

- Rebuilt Steering Box

Rear Suspension

- New Spring Bushings

- New Nylon Leaf Spring Inserts

- Three Quarter Inch Swal Bar

- Gabriel Gas Shocks

Wheels

- Dayton “Knock-Off” Wire Wheels (Bead lace) Cost $2500.00

- Wheel Size: 15”X 6”

- Stainless Steel Spokes/Nipples

- Clear Powder Coated

Tires

- P205 SR75-15 (Dunlop SP-40) White Walls

Rear Axle

- 3;07:1 twin Traction Dana 44 Differential (Synthetic Oil)

- New Axles and Bearings.

- Rear Axle backing Plates have been replaced with “flanged Axle Backing Plates.  Note: The rear hub, axle and bearings is now removed as an assembly (The backing plate stays in place).  This allows the axle to be separated from the hub with a hydraulic press

- New Brake Drums installed March 1966

Engine

- 350 C.I. Small Block Chevrolet engine.  High Energy Engine by racing Head Service:  8.5:1 compression ratio and mild 252 degree cam Profile. 220 estimated HP.

- Edelbrock Performer aluminum intake manifold.

- Edelbrock 1406 (600 cfm) Carburetor

- Chromed R3 Carb enclosure ( Carburetor fires are a thing of the past)

- March Polished aluminum underdrive pulleys ( 5 inch diameter crank pulley)

- B&M 2 piece aluminum valve covers

- Sanderson Ceramic Block hugger headers

- 80 amp one wire Alternator

- Electric Fuel Pump and electric shut-off valve.  Both controlled by a hidden , disable switch

- Both fuel pump and fuel shutoff are conrolled by the ignition switch.

- GM HEU Distributor

- Taylor Spiro-Pro Ignition Wires.

- Polished Stainless Steel Flex Fan

- Auxilliary Electric Cooling fan (Manually Controlled)

- Polished Aluminum Coolant reciovery Tank

- Chromed GN A-6 Air Conditioning Compressor

- Carb Air Filter relocated to right wheel Well

- Chrome high Volume Water Pump

- Battery Cut-Off Switch

Transmission

- Chevrolet 700R4 Four Speed Automatic ( Fourth Gear: 30% overdrive)

- Toeque Converter will Lock up at 37 MPH

- Torque Converter wil unlock when throttle is 7/8 open.

Wiring harness

- No longer routed through engine compartment

- All forward wiring is through right wheel well

Head lamps

- Quartz halogen sealed beam headlights

- The headlights are powered by 4 relays

- Each function has a relay of it’ own

Brake/Turn Signal lamps

- There are 2 dual filament lamps in each tail lanp housing

- Four 30 amp relayts are used to power the rear lamps

- Two relays furnish power to each tail lamp

- One relay furnished power to the tail lamp filaments, while the other relay furnishes power to the brake/turn signals filaments

Power Windows

- New Motor, both sides

- Each motor received full voltage via three relays that react to the up/down switch

Fuel System

- Electric Fuel Pump and Electric Fuel Shut-Off Valve

Sound system

- Sony AM/FM Cassette Stereo

- Two Channel Only

- Fully Automatic Electric Antenna

Cruise Control

- Electronic /vacuum

- Tap up/down feature in ½ mile increments

- Control head incorporated into turn signal lever

- All wiring concealed and routed through the Steering Column ( looks OEM)

- Servo and Electronic Control module mounted inside the car below the dash

Dash Pad

- New dash Pad installed in 1982

- Original Cover on Glove Box

Instruments

- Tachometer and Speedometer replaced by Autometer gauges

- Clock has been replaced with a Quartz Unit

- All other instruments are original

- Instrument panel made from real wood that matches the steering wheel

Steering Wheel

- Italian made – Personal Wooden Steering Wheel

Upholstery

- All new.  Matches original Style and original Fawn and Elk color

Front Seats

- High Back bucket seats, salvaged from 87 Dodge Daytona.  Have been reupholstered to match original

Gas Filler Door

- Gas Filler Door has been replaced with a “flip Open” style gas Cap molded into the body. The true gas cap is concealed under the “Flip Open” cap

Hood

- Added second hood support to the right side

- Filled in Hood edge to maintain a 3/16” gap around hood

Trunk Lid

- Replaced Studebaker script with Avanti script

- Filled in trunk edges to maintain a 3/16” gap around runk

- Inside of trunk Lid is autographed by Tom Kellog and John Epstein

Doors

- Rebuilt hinge pins / bushings

- Filled in door edged to maintain a 3/16” gap around doors